## Slide 1: ESCRA Forklift Training

## Slide 2: ESCRA Forklift Training
Why Forklift Training Is Necessary
  100 fatalities each year
  20,000 lost workday injuries annually
  Common injuries
    Hitting a pedestrian
    Tipping over
    Falling from raised forks
    Falling from a ladder struck with a forklift
    Falling material
    Training reduces injuries

## Slide 3: ESCRA Forklift Training

## Slide 4: ESCRA Forklift Training
  Basic Forklift rules
    Don’t stand or pass under raised forks.
    Only handle stable loads within truck’s rated capacity.
    Use a safety platform to lift people.
    Only use approved trucks in hazardous locations.
    Lower forks, neutralize controls, shut off engine, and
    set brakes when truck is unattended

## Slide 5: ESCRA Forklift Training
While in the Operator Seat
  Make nonmoving checks—gauges, lights,
  horn, backup alarm, warning light, tilt and
  lift mechanism, and parking brake
  Make moving checks—seat belt, running
  brakes, and steering
  Operator visibility
    Loads can restrict vision.
    Look in the direction of travel.
    Check blind spots.

## Slide 6: ESCRA Forklift Training
  Attachments
    Attachments act like extensions to the length
    or width of the forklift and, therefore, require
    additional operating clearance.
    Adding an attachment is like permanently carrying
    a load. If the attachment weighs 1,000 pounds (lb),
    your forklift’s capacity is automatically reduced by
    1,000 lb.
    Attachments typically move the load farther away
    from the forklift, which increases your load center.
    If the attachment moves the load 8 in. away, it will
    reduce the capacity by approximately 800 lb (100 lb per in.)
    because loads that normally have a load center of 24 in.
    now have a 32-in. load center.

## Slide 7: ESCRA Forklift Training
Unintentional, mistaken operation
can cause serious accidents
A 5,000-pound forklift at 10 mph with
a 4,000 pound load has a potential
destructive force of 135,000 pounds
of energy.